A Behavioral HDL Description of Forward AES-128 Encryption
Preston Pitzer [1]
## Introduction
Advanced Encryption Standard (AES) is a substitution-permutation network private-key block cipher, designed as a successor to DES by John Daemen and Vincent Rijman [1]. The use of a substition-permutation network makes it highly efficient to implement in hardware, and the use of Galios Fields can be significantly simplified in hardware down to simple XOR operations. The x86 instruction set contains several instructions relating to AES encryption and decryption, including AESENC, which implements a single non-final round of AES encryption (final round is handled by AESENCLAST).
The AES cryptosystem relies on several submodules, each of which can be implemented (optionally) combinationally. The first of these is the SubBytes module, which reads byte(s) and returns a transformed byte (the input’s multipliative inverse on GF(8) through an affine transform). The second is ShiftRows, a byte-wise ciruclar left shift, the magnitude of the shift being dependent on the Row’s index. The third is MixColumns, which performes modular reduction on a column down to a 4th order polynomial with coefficients in GF(2), and then multiplies by a fixed polynomial. Practically, this corresponds to a multiplication of the input row by a fixed 4x4 matrix (in the 128 bit case). Finally, the round key (explained later) is bitwise XORd against the flattened matrix. The state controller handles construction of the data matrix and key from a 32-bit data line input, cycling through 10 rounds of the AESENC flow, and then returning the ciphertext through the 32-bit output line.
## Module Descriptions
### data_mat
The primary “data structure” for AES-128 is a 4x4 column major matrix of bytes, the individual bits of which represent coefficients of elements of GF(28). Because we have chosen to work with a 32 bit-bus length, this module should allow for reading and writing of an arbitrary row or column. To this end, the module has a 32-bit data in, 2 bits for index, 1 bit for row/column selection, 1 bit for read/write, and a write_enable. It has a single 32 bit output vector.

### d