A Behavioral HDL Description of Forward AES-128 Encryption
Preston Pitzer [1]
## Introduction
Advanced Encryption Standard (AES) is a substitution-permutation network private-key block cipher, designed as a successor to DES by John Daemen and Vincent Rijman [1]. The use of a substition-permutation network makes it highly efficient to implement in hardware, and the use of Galios Fields can be significantly simplified in hardware down to simple XOR operations. The x86 instruction set contains several instructions relating to AES encryption and decryption, including AESENC, which implements a single non-final round of AES encryption (final round is handled by AESENCLAST).
The AES cryptosystem relies on several submodules, each of which can be implemented (optionally) combinationally. The first of these is the SubBytes module, which reads byte(s) and returns a transformed byte (the input’s multipliative inverse on GF(8) through an affine transform). The second is ShiftRows, a byte-wise ciruclar left shift, the magnitude of the shift being dependent on the Row’s index. The third is MixColumns, which performes modular reduction on a column down to a 4th order polynomial with coefficients in GF(2), and then multiplies by a fixed polynomial. Practically, this corresponds to a multiplication of the input row by a fixed 4x4 matrix (in the 128 bit case). Finally, the round key (explained later) is bitwise XORd against the flattened matrix. The state controller handles construction of the data matrix and key from a 32-bit data line input, cycling through 10 rounds of the AESENC flow, and then returning the ciphertext through the 32-bit output line.
## Module Descriptions
### data_mat
The primary “data structure” for AES-128 is a 4x4 column major matrix of bytes, the individual bits of which represent coefficients of elements of GF(28). Because we have chosen to work with a 32 bit-bus length, this module should allow for reading and writing of an arbitrary row or column. To this end, the module has a 32-bit data in, two 2-bit vectors for selecting the input and output row/column, a write enable, and connections to clk and reset. When write enable is high, the selected row or columns is overriten by the value at the input (which is multiplexed in the top-level module).

Notice how in the test, the second byte (index 1) in row 0 is overwritten by the write made to the second column, and this is reflected in the read operation on row 0.
ShiftRows
The ShiftRows module combinationally implements the ShiftRows operation, which is a circular left shift byte-wise by idx, where idx is the row being shifted.
### The test shows correct implementation of the shift.

SubBytes
### This module implements the “substitution” in the substitution-permutation network. Mathematically, polynomials are being replaced with their multiplicative inverse. In our case however, it is simply implemented as a lookup table (LUT), due to the impracticality of calculating the inverse over GF(2­8) in digital logic.
 (Image from Wikipedia https://en.wikipedia.org/wiki/Rijndael_S-box)
### MixColumns
This module “mixes” an input column by multiplying it by a fixed matrix. I’ve implemented it using only multiplexers, shifts, and XORs for speed. A multiplication by 2 in our Galios Field is equivalent to a left shift and conditional XOR with the byte 8’h1b, and a multiplication by 3 is a multiplication by 2 XOR the original byte. Because the matrix only contains the values {1,2,3}, these are the only operations we need.
Because this module has a greater complexity (and the tools to calculate this manually are not easilly accessible wtihin the systemverilog syntax) compared to the preceeding ones, the output was evaluated against known test vectors for this module, provided by NIST.

### Key_expand
The key_expand module handles the generation of the round keys from the original cipher during the AES encryption scheme. In AES-128, the cipher key is 128 bits long, and from the cipher key, 11 round keys are generated (the first of which being the original cipher key). Each subsequent round key is generated by performing bit manipulations on the previous key. The manipulations in order are a circular left shift of one word (word = 32 bits), a bytewise sbox substitution fot the entire key, a xor operation with a round constant that varies between each round key, and finally extra xor operations with the previous key. Each of these operation are encapsulated as separate functions in my module and then are called upon during the key expansion stage as necessary.
The inputs to the key_expand module include the clock, reset, the cipher key (32 bits at a time), a start signal, and indexing variables to determine which portion of which round key to output (32 bits at a time). The outputs of the system are a done signal to signify all round keys are generatedand the round key itself (in 32 bit segments). Following a start pulse, the key_expand module pulls in a quarter of the cipher key at a time, (32 bits) MSB first. Once it is done loading the cipher key, it generates each round key in 10 stages and then outputs a high sone signal. Each round key takes 1 clock cycle to complete such that all of the sbox, round key, and shifting hardware can be reused during each round key generation (area prioritization).
Verification:
Using the testbench key_expand_tb I verified my design using a cipher key I found in an online example that includes all of the correct round key ouptuts. I also tested various conditions with consecutive starts, holds, and restarts to ensure the design works robustly. Here is the output from my test next to the online round key outputs:

Figure 1: key_expand Output	Figure 2: Valid Output

State Manager
The state manager controls the flow of data throughout the system, primarily by controlling which row and column is written to and read from the data matrix. Each of the above modules have a designated “state”, which in a literal sense is actually 4 states, because each operation is performed on the entire matrix, one row or column at a time. In addition to these, the module as an idle state, which awaits an active-low start signal being asserted. Once the signal is asserted, the following 8 cycles load the plaintext and then the initial key as 32-bit words. Then, the state manager awaits the signal from the key_expansion module that indicates that all of the round keys are ready. Then for 9 rounds, the flow of SubBytes, ShiftRows, MixColumns, and AddRoundKey is executed on the matrix. On the final round, the MixColumns step is omitted. Following this, the system enters a pseudo-idle state where a “start read” signal is asserted. The encrypted ciphertext is then asserted to the 32-bit output line over the next 4 clock cycles.
This module is validated at the level of inspection via GTKwave.